## Slide 1: Computer Architecture
Part I Boolean Algebra and Map Simplifications
Department of Computer Science, Faculty of Science, Chiang Mai University

## Slide 2: Outline
Logic Gates
Boolean Algebra
Map Simplification

## Slide 3: Boolean Function
A Boolean function can be expressed algebraically with binary variables, the logic operation symbols, parentheses, and equal sign.
To represent a function in a truth table we need a list of the 2n combinations of the n binary variables.

## Slide 4: Truth Table and Logic Diagram for F = x + yz
Sum of Minterm
F(x, y, z) = (1, 4, 5, 6, 7)

## Slide 5: Two Graphic Symbols for NOR gate
DeMorgan’s theorem

## Slide 6: Two Graphic Symbols for NAND gate
DeMorgan’s theorem

## Slide 7: Boolean Algebra Manipulation
F = ABC + ABC’ + A’C
= AB (C + C’) + A’C
= AB (1) + A’C
= AB + A’C
By manipulating a Boolean expression according to Boolean algebra rules, one may obtain a simpler expression that will require fewer gates.

## Slide 8: Two Logic Diagrams for the Same Boolean Function

## Slide 9: Two Logic Diagrams for the Same Boolean Function

## Slide 10: K-Map (Karnaugh Map)
The squares corresponding to minterms that produce 1 for the function are marked by a 1 and the others are marked by a 0 or are left empty.
The squares containing 1’s are combined in groups of adjacent squares.
These groups must contain a number of squares that is an integral power of 2.

## Slide 11: Maps for Two-Variable Functions
B
A

## Slide 12: Maps for Three-Variable Functions
B
A
C
C

## Slide 13: Maps for Four-Variable Functions

## Slide 14: Map for F(A, B, C) = (3, 4, 6, 7)
F = BC + AC
The squares at the extreme ends of the same horizontal row are also to be considered adjacent.
two squares are adjacent if they share an edge.
The OR of all terms gives the simplified algebraic expression.

## Slide 15: Map for F(A, B, C) = (0, 2, 4, 5, 6)
F = C + AB
Groups of combined adjacent squares may share one or more squares with one or more groups.

## Slide 16: Map for F(A, B, C, D) = (0, 1, 2, 6, 8, 9, 10)
Sum-of-Products
F = BD + BC + ACD
The squares at the top and the bottom of a column are adjacent.
The four corner squares of a map must also be considered to be adjacent.

## Slide 17: Product-of-Sums Simplification
If we mark the empty squares with 0’s and combine them into groups of adjacent squares, we obtain the complement of the function (F’).
Taking the complement of F’ produces an expression for F in product-of-sums form.

## Slide 18: Map for F(A, B, C) = (0, 1, 2, 5, 8, 9, 10)
Product-of-Sums
F = AB + CD + BD
F = (A + B)(C + D)(B + D)

## Slide 19: Logic Diagrams with 3 ANDs and 1 OR Gates

## Slide 20: Logic Diagrams with 3 ORs and 1 AND Gates

## Slide 21: Logic Diagrams with 4 NANDs

## Slide 22: Logic Diagrams with 4 NORs

## Slide 23: Don’t-Care Conditions F(A, B, C) = (0, 2, 6) d(A, B, C) = (1, 3, 5)
F = A + BC
F(A, B, C) = (0, 1, 2, 3, 6)
The don’t care condition may be assumed to be either 0 or 1.

## Slide 24: Reference
M. Moris Mano, Computer System Architecture, 3rd ed. NJ: Prentice Hall, 1992.