## Slide 1: Computer Architecture
Part V
Arithmetic Algorithms and Memory Address Map
Department of Computer Science, Faculty of Science, Chiang Mai University

## Slide 2: Outline
Signed-Magnitude Addition and Subtraction
Multiply Operation
Memory Address Map for Microprocessor

## Slide 3: Hardware for Signed-Magnitude Addition and Subtraction
It consists of register A and B and sign flip-flop As and Bs.
Subtraction is done by adding A to the 2’s complement of B.
The output carry is transferred to flip-flop E, where it can be checked to determine the relative magnitudes of the two numbers.
The add-overflow flip-flop AVF holds the overflow bit when A and B are added.

## Slide 4: Hardware for Signed-Magnitude Addition and Subtraction
The addition of A plus B is done through the parallel adder.
The S (sum) output of the adder is applied to the input of the A register.
The complementer provides and output of B or the complement of B depending on the state of the mode control M.

## Slide 5: Hardware for Signed-Magnitude Addition and Subtraction
When M = 0, the output of B is transferred to the adder, the input carry is 0, and the output of the adder is equal to the sum A + B.
When M = 1, the 1’s complement of B is applied to the adder, the input carry is 1, and output S = A + B + 1 = A – B.

## Slide 6: Hardware for Signed-Magnitude Addition and Subtraction

## Slide 7: Hardware Implementation
A and B are registers.
AS and BS are sign flip-flops.
E is an output carry flip-flop.
EA is a register that combines E and A.
AVF is an add-overflow flip-flop.
S is sum.
M is mode control.
  M = 0, A + B + 0 = A + B
  M = 1, A + B̅ + 1 = A – B

## Slide 8: Multiplication Algorithm

## Slide 9: Hardware for Multiply Operation
The multiplier is stored in the Q register and its sign in Qs.
The sequence counter SC is initially set to a number equal to the number of bits in the multiplier.
The counter is decremented by 1 after forming each partial product.
When the content of the counter reaches zero, the product is formed and the process stops.

## Slide 10: Hardware for Multiply Operation
Initially, the multiplicand is in register B and the multiplier in Q.
The sum of A and B forms partial product which is transferred to the EA register.
Both partial product and multiplier are shifted to the right.
The 0 is shifted into E.

## Slide 11: Hardware for Multiply Operation
After the shift, one bit of the partial product is shifted into Q, pushing the multiplier bits one position to the right.
In this manner, the rightmost flip-flop in register Q, designated by Qn, will hold the bit of the multiplier, which must be inspected next.

## Slide 12: Hardware for Multiply Operation

## Slide 13: Numerical Example for Binary Multiplier

## Slide 14: Main Memory
RAM is used for storing the bulk of the programs and data that are subject to change.
ROM is used for storing programs that are permanently resident in the computer and for tables of constants that do not change in value once the production of the computer is completed.

## Slide 15: Typical RAM chip
The capacity of the memory is 128 words of eight bits (one byte) per word.
This requires a 7-bit address and an 8-bit bidirectional data bus.
The read and write inputs specify the memory operation and the two chips select (CS) control inputs are for enabling the chip only when it is selected by the microprocessor.

## Slide 16: Typical RAM chip
The function table listed in slide number 31 specifies the operation of the RAM chip.
The unit is in operation only when CS1 = 1 and CS2 = 0.
If the chip select inputs are not enabled, or if they are enables but the read or write inputs are not enabled, the memory is inhibited and its data bus is in a high-impedance state.

## Slide 17: Typical RAM chip

## Slide 18: Typical ROM chip

## Slide 19: Memory Address Map for Microprocessor
The component column specifies whether a RAM or a ROM chip is used.
The hexadecimal address column assigns a range of hexadecimal equivalent addresses for each chip.
The small x’s under the address bus lines designate those lines that must be connected to the address inputs in each chip.

## Slide 20: Memory Address Map for Microprocessor
The RAM chips have 128 bytes and need seven address line.
The ROM chip has 512 bytes and needs 9 address line.
We choose bus lines 8 and 9 to represent four distinct binary combinations.
Note that any other pair of unused bus lines can be chosen for this purpose.

## Slide 21: Memory Address Map for Microprocessor
The distinction between a RAM and ROM address is done with another bus line.
Here we choose line 10 for this purpose.
The equivalent hexadecimal address for each chip is obtained from the information under the address bus assignment.

## Slide 22: Memory Address Map for Microprocessor
The address bus lines are subdivided into groups of four bits each so that each group can be represented with a hexadecimal digit.
The x’s represent a binary number that can range from an all-0’s to an all-1’s value.

## Slide 23: Memory Address Map for Microprocessor

## Slide 24: Reference
M. Moris Mano, Computer System Architecture, 3rd ed. NJ: Prentice Hall, 1992.