## Slide 1: Assembly Language
Part V Branching Structures
Department of Computer Science, Faculty of Science, Chiang Mai University

## Slide 2: Outline
An Example of a Jump
Conditional Jumps
Branching Structures

## Slide 3: IBM Character Display

## Slide 4: Conditional Jumps
Jxxx destination_label
Jump instructions themselves do not affect the flags.
destination_label must precede the jump instruction by no more than 126 bytes, or follow it by no more than 127 bytes.

## Slide 5: The CMP (compare) Instruction
CMP destination, source
CMP is just like SUB, except that destination is not changed.

## Slide 6: How the CPU Implements a Conditional Jump
CMP AX, BX ; AX = 7FFFh, BX = 0001h
JG BELOW ; AX – BX = 7FFEh
ZF = 0
SF = 0
OF = 0
ZF = 0 and SF = OF
0111 1111 1111 1111
– 0000 0000 0000 0001
0111 1111 1111 1110

## Slide 7: Signed Versus Unsigned Jumps
Suppose we’re giving a signed interpretation.
Using the wrong kind of jump can lead to incorrect results.
CMP AX, BX ; AX = 7FFFh, BX = 8000h
JA BELOW
7FFFh > 8000h in a signed sense, the program does not jump to BELOW.
7FFFh < 8000h in an unsigned sense, and we are using the unsigned jump JA.

## Slide 8: Suppose AX and BX contain signed numbers. Write some code to put the biggest one in CX.
MOV CX, AX ; put AX in CX
CMP BX, CX ; is BX bigger?
JLE NEXT ; no, go on
MOV CX, BX ; yes, put BX in CX
NEXT:

## Slide 9: The JMP Instruction
The JMP (jump) instruction causes an unconditional transfer of control (unconditional jump).
JMP destination
JMP can be used to get around the range restriction of a conditional jump.

## Slide 10: Unconditional Jump
TOP:
; body of the loop
DEC CX ; decrement counter
JNZ TOP ; keep looping if CX > 0
MOV AX, BX
; the loop body contains so many instructions that label TOP is out of range for JNZ (more than 126 bytes before JMP TOP)

## Slide 11: Unconditional Jump
TOP:
; body of the loop
DEC CX ; decrement counter
JNZ BOTTOM ; keep looping if CX > 0
JMP EXIT
BOTTOM:
JMP TOP
EXIT:
MOV AX, BX

## Slide 12: IF-THEN
IF condition is true
THEN
execute true-branch statements
END_IF

## Slide 13: Replace the number in AX by its absolute value.
IF AX < 0
THEN
replace AX by –AX
END_IF

## Slide 14: Replace the number in AX by its absolute value.
; if AX < 0
CMP AX, 0 ; AX < 0 ?
JNL END_IF ; no, exit
; then
NEG AX ; yes, change sign
END IF:

## Slide 15: IF-THEN-ELSE
IF condition is true
THEN
execute true-branch statements
ELSE
execute false-branch statements
END_IF

## Slide 16: Suppose AL and BL contain extended ASCII characters. Display the one that comes first in the character sequence.
IF AL <= BL
THEN
display the character in AL
ELSE
display the character in BL
END_IF

## Slide 17: Suppose AL and BL contain extended ASCII characters. Display the one that comes first in the character sequence.
MOV AH, 2 ; prepare to display
; if AL <= BL
CMP AL, BL ; AL <= BL?
JNBE ELSE_ ; no, display char in BL
; then ; AL <= BL
MOV DL, AL ; move char to be displayed
JMP DISPLAY ; go to display
ELSE_: ; BL < AL
MOV DL, BL
DISPLAY:
INT 21h ; display it
END_IF

## Slide 18: CASE
CASE expression
value 1 : statements_1
value 2 : statements_2
.
.
.
value n : statements_n
END_CASE

## Slide 19: If AX contains a negative number, put –1 in BX; if AX contains 0, put 0 in BX, if AX contains a positive number , put 1 in BX.
CASE AX
<0 : put –1 in BX
=0 : put 0 in BX
>0 : put 1 in BX
END_CASE

## Slide 20: If AX contains a negative number, put –1 in BX; if AX contains 0, put 0 in BX, if AX contains a positive number , put 1 in BX.
; case AX
CMP AX, 0 ; test AX
JL NEGATIVE ; AX < 0
JE ZERO ; AX = 0
JG POSITIVE ; AX > 0
NEGATIVE:
MOV BX, -1 ; put -1 in BX
JMP END_CASE ; and exit
ZERO:
MOV BX, 0 ; put -0in BX
JMP END_CASE ; and exit
POSITIVE:
MOV BX, 1 ; put 1 in BX
END_CASE:

## Slide 21: If AL contains 1 or 3, display “o”; If AL contains 2 or 4, display “e”.
CASE AL
1, 3 : display “o”
2, 4 : display “e”
END_CASE

## Slide 22: If AL contains 1 or 3, display “o”; If AL contains 2 or 4, display “e”.
; case AL
; 1,3 :
CMP AL, 1 ; AL = 1?
JE ODD ; yes, display ‘o’
CMP AL ,3 ; AL = 3?
JE ODD ; yes, display ‘o’
; 2,4 :
CMP AL, 2 ; AL = 2?
JE EVEN ; yes, display ‘e’
CMP AL, 4 ; AL = 4?
JE EVEN ; yes, display ‘e’
JMP END_CASE ; not 1..4

## Slide 23: If AL contains 1 or 3, display “o”; If AL contains 2 or 4, display “e”.
ODD: ; display ‘o’
MOV DL, ‘o’ ; get ‘o’
JMP DISPLAY ; go to display
EVEN: ; display ‘e’
MOV DL, ‘e’ ; get ‘e’
DISPLAY:
MOV AH, 2
INT 21H ; display char
END_CASE:

## Slide 24: Reference
Ytha Yu and Charles Marut, Assembly Language Programming and Organization of the IBM PC. New York: McGraw-Hill, 1992.